## Slide 1
모터 데이터 분석 - Feature Importance
한국전자기술연구원
Rev.0
지능메카트로닉스연구센터
이정환 연구원
2024.04

## Slide 2: Analysis Pipeline - 1
🔹 Data Preparation
30 vibration datasets (X, Y, Z axes + Timestamp)
Each dataset has a different length
→ truncated to fixed length (99,000 samples) → 1 Chunk = 55 seconds (1,800 Hz × 55 sec)
🔹 Time Domain
Extracted features (per-axis statistics): Mean, Std, Variance, Skewness
X/Y/Z 3 axes × 4 features = 12 Features
Result: (30, 12) Feature Matrix
🔹 Frequency Domain
Sampling frequency: 1,800 Hz
Operating frequency: 900 Hz
FFT-based Harmonic Feature extraction (0~35 → total 36 features)
Use Feature Importance to select top 12 features only -> prevent overfitting

## Slide 3: Analysis Pipeline - 2
🔹 Model Training
RandomForestClassifier (n=100)
Data split: Train/Test = 7:3
Cross-validation (cv=5) → Accuracy evaluation
🔹 Overall Process
Data loading & fixed-length truncation
Time-domain feature extraction (12 features)
Frequency-domain feature extraction (36 → top 12 selected)
Construction of Feature Matrix (X_data, y_data)
Random Forest training & performance evaluation

## Slide 4
Timestamp
X
Y
Z
Timestamp
X
Y
Z
Timestamp
X
Y
Z
…
df[0].shape = (107346, 4)
df[1].shape = (102909, 4)
df[2].shape = (117343, 4)
∙
∙
∙
df[29].shape = (101405, 4)
df[0].shape = (99000, 4)
df[1].shape = (99000, 4)
df[2].shape = (99000, 4)
∙
∙
∙
df[29].shape = (99000, 4)
df.iloc[:99000, ::]
Time domain
df[0]
df[1]
df[29]
1, 99000, 3
Timestamp
X
Y
Z
x_mean
y_mean
z_std
x_std
x_var
y_std
y_var
z_mean
z_var
x_skew
y_skew
z_skew
Ⅹ 30개
1, 99000, 3 -> 1 ,12
1 ,12 -> 30, 12
X_train, X_test, y_train, y_test = train_test_split(X_data, y_data, test_size=0.3)
X_data.shape = 30, 12
Y_data.shape = 30, 1
rf = RandomForestClassifier(n_estimators = 100)
y_pred_cv = cross_val_predict(rf, X_train, y_train, cv =5)
y_pred = np.argmax(y_pred_cv, axis = 1)
accuracy = accuracy_score(y_test, y_pred)
chunk_size = 99000 (1800 (sampling_frequency)*55개)
x_mean
y_mean
z_std
x_std
x_var
y_std
y_var
z_mean
z_var
x_skew
y_skew
z_skew
label
1
2
3
30
〮
〮
〮
〮
〮
〮
〮
〮
〮
Statistical Features 추출(mean, std, var, skew)
30개의 진동데이터
chunk_size로 나누기

## Slide 5
Timestamp
X
Y
Z
Timestamp
X
Y
Z
Timestamp
X
Y
Z
…
df[0].shape = (107346, 4)
df[1].shape = (102909, 4)
df[2].shape = (117343, 4)
∙
∙
∙
df[29].shape = (101405, 4)
df[0]
df[1]
df[29]
Frequency domain
운전주파수 900 Hz
샘플링 주파수 1800 Hz
Ex) f(0) = 50Hz(Harmonic Feature)
X(0), X(1), … , X(35)
df[0].shape = (99000, 4)
df[1].shape = (99000, 4)
df[2].shape = (99000, 4)
∙
∙
∙
df[29].shape = (99000, 4)
df.iloc[:99000, ::]
Chunk_size = 99000 (1800Hz (sampling_frequency)*55개)
label
〮
〮
〮
1
2
3
30
〮
〮
〮
〮
〮
〮
X(0), X(1), X(2), X(3), … , X(34), X(35)
X(0), X(1), X(2), X(3), … , X(34), X(35)
너무 많은 특성을 사용하면 과적합 발생
과적합을 방지하기 위하여 feature importance을
사용하여 상위 중요도 12개만 사용
X(0), X(10), X(12), X(23), … , X(27), X(35)
1
2
3
30
〮
〮
〮
〮
〮
〮
총 36개 특성
총 12개 특성
X_train, X_test, y_train, y_test =
train_test_split(X_data, y_data, test_size=0.3)
X_data.shape = 30, 12
Y_data.shape = 30, 1
. . .
rf = RandomForestClassifier(n_estimators = 100)
y_pred_cv = cross_val_predict(rf, X_train, y_train, cv =5)
y_pred = np.argmax(y_pred_cv, axis = 1)
accuracy = accuracy_score(y_test, y_pred)
30개의 진동데이터
chunk_size로 나누기

## Slide 6
기업과 함께 성장하는 최고의 파트너
전자∙IT분야 글로벌 전문생산연구기관